## Slide 1
The Loner M6 Safety System

## Slide 2
CONTENTS
About the device
Starting your shift
During your shift
Generating Manual Alerts
Receiving a voice call
Ending your shift
Questions?

## Slide 3
ABOUT THE DEVICE
Notes: Is there any questions so far?
So now we’re going to talk about the physical components on each of the device so you can get familiar with the parts you’ll be interacting with while using it.

## Slide 4
ABOUT THE DEVICE
There are three primary mechanical components of the Loner device.
Belt Clip
Latch
SureSafe monitoring light
and power button
Notes: The Loner device has three primary components. The power, the belt clip, and the latch. We’ll talk more about how you’ll interact with these in the next section.

## Slide 5
STARTING YOUR SHIFT
Notes: Questions?
So now we’re going to talk about what you’re going to do when starting your shift and discuss how to properly set up and turn on your devices for proper use.

## Slide 6
Press the power button
The green SureSafe light will blink until it is connected to the Blackline Safety Network.
Once connected, the light will be SOLID GREEN.
This means your safety is
now monitored.
STARTING YOUR SHIFT
TURNING ON YOUR LONER

## Slide 7
Clip the device to the side of your hip or to your chest pocket
STARTING YOUR SHIFT
WEARING YOUR LONER
Notes: Once you have turned the device on all that’s left to do is clip the device to your hip pocket, which is the recommended placement of the device.

## Slide 8
Do not leave Loner unattended when powered on
This can lead to false alerts
STARTING YOUR SHIFT
Notes: Wearing the device is an important part of the Loner device’s functionality. While Loner device is on, NEVER leave unattended. The automatic alerts on the device (such as No Motion) can be activated and cause false alerts.

## Slide 9
DURING YOUR SHIFT
Notes: .

## Slide 10
During your shift, the device may ask you to confirm that you are OK when it detects one of the following:
No-motion
Fall detection
Check-in
DURING YOUR SHIFT
AUTOMATIC FEATURES

## Slide 11
No-motion
Fall Detection
Check-in
DURING YOUR SHIFT
Pending Alarm
If you’re OK press the confirm button on the latch
This returns Loner to normal function.
No notification is sent.
AUTOMATIC FEATURES – IF YOU’RE OK

## Slide 12
No-motion
Fall Detection
Check-in
DURING YOUR SHIFT
Pending Alarm
If you can’t press the confirm button after a certain period of time, the device will go into high alarm
This sends an alert notification
The high alarm can be silenced by pressing and holding the button. The alert notification still remains active.
Once an alert is acknowledged by monitoring personnel, the loner will display a blue light
AUTOMATIC FEATURES – IF YOU CAN’T CONFIRM

## Slide 13
To do this, press and hold the latch for two vibrations. This will reset the check-in timer before the automatic alarm sounds.
Your device will automatically check you in if you are driving over 35 km/h.
00:54:34
2:00:00
Before pre-check in
Check-in timer reset
DURING YOUR SHIFT
PRE CHECK-IN

## Slide 14
Emergency alert
(Audible)
Silent alert
During your shift, you may need to request help using one of the manual features:
DURING YOUR SHIFT
MANUAL FEATURES

## Slide 15
Emergency alert
An alert notification will be sent to monitoring personnel
DURING YOUR SHIFT
The high alarm can be silenced by pressing and holding the button. The alert notification still remains active.
Once an alert is acknowledged by monitoring personnel, the loner will display a blue light
Request help by pulling down the latch

## Slide 16
Silent Alert
Press the confirm button until the vibration stops
(two full vibration pulses ~5 sec.)
(No audible or visual alarm is generated on the Loner device)
DURING YOUR SHIFT
An alert notification will be sent to monitoring personnel
No alert acknowledged blue light
will be displayed on the device during a silent alert even if monitoring personnel have acknowledged the incident

## Slide 17
RECEIVING A VOICE CALL

## Slide 18
A voice call can be made by monitoring personnel directly to the device. After an alert is triggered the device will beep once when a call is connected.
This is the safety monitoring center. We had an alert from your device.
*BEEP*
RECEIVING A VOICE CALL
That was a false alarm. I do not require assistance.
Understood. I will go ahead and resolve your alert.
*BEEP*
Once the call is connected you can speak back and forth to monitoring personnel. When the call has ended the device will beep once more.
RECEIVING A VOICE CALL

## Slide 19
When a silent alert is generated, monitoring personnel can still connect with the Loner device. However the Loner will not beep and it will be in a ‘listen only’ mode.
RECEIVING A VOICE CALL
RECEIVING A VOICE CALL – AFTER A SILENT ALERT
…

## Slide 20
NOTIFICATIONS

## Slide 21
Link lost alarm
Your Loner will notify you if it loses cellular communication.
Your Loner SureSafe light will begin blinking to confirm that your safety is not being monitored.
If configured, the device may initiate a link lost alarm.
SureSafe monitoring light
BLINKING
NOTIFICATIONS
Low battery alarm
Your Loner device is configured to signal to you when the battery falls below a certain configured percentage
Low battery alarm is characterized by a short beep and a quick flash every 5 minutes. Charge your device as soon as possible.

## Slide 22
ENDING YOUR SHIFT

## Slide 23
Press the power button until beeping and vibration stops (usually 3 seconds)
The device will begin its shutdown sequence and the SureSafe light will flash and then turn off once your Loner logs off from the Blackline Safety Network.
ENDING YOUR SHIFT
Your safety is no longer being monitored
TURNING OFF YOUR LONER DEVICE
Notes: At the end of your shift, remove the loner from your hip and press and hold the power button for about 3 seconds. The device will go into shutdown sequence. The green light on the Loner device may flash for up to 10 minutes while it disconnects.

## Slide 24
Full charge takes approx 4 hours
Battery Life is 20 hours
Insert the charger into the bottom of the device and connect to power source
While the device is charging the red lights on the base will flash
When Loner is charged, the red lights will turn on continuously.
ENDING YOUR SHIFT
CHARGING YOUR LONER
Notes: It is recommended that you charge your Loner device after every use. Simply plug the charger into the bottom of device, while it’s charging red lights will flash at the base of the device and once it’s fully charged, these lights will be solid red. Charging Loner device from fully dead takes approximately 4 hours.

## Slide 25
QUESTIONS?

## Slide 26
For more support materials,
Please visit support.blacklinesafety.com
Customer Care: 1-877-869-7212
0045/R4/2016-06-01