## Slide 1
www.BlacklineSafety.com

## Slide 2: INTRODUCTION
WHO IS BLACKLINE SAFETY?
Headquartered in Calgary, Alberta, Canada
Global connected safety technology leader behind G7
Our talented team of designers and engineers create and manufacture everything in-house
In-house Safety Monitoring Center and Customer Care
We offer services in over 100 countries
Currently monitor over 25,000 employees around the world
We have recorded 26.5 million hours of equipment use and have managed over 850,000 customer alerts

## Slide 3: INTRODUCTION
WHAT IS G7?
Work-everywhere, wearable, personal safety monitor with gas detection
18 hours battery
2-way texting
2-way voice communication (available to purchase)
Deliver instant situational awareness
Intrinsically Safe
Standard
Single
Quad

## Slide 4: INTRODUCTION
SERVICE PLANS
Self-monitored
Your team monitors your Blackline Live account
Blackline Monitored
Blackline Safety’s in-house monitoring personnel monitor your team 24/7, 365 days a year
99.5% of alerts responded to in under 1 minute

## Slide 5
HARDWARE DETAILS

## Slide 6: POWER ON
Press the power button once to turn the device on.
SURESAFE LIGHT
A solid SureSafe Light means you are connected to the Blackline Safety Network.
A blinking SureSafe Light means your device is trying to connect. Don’t panic! It’s OK to have a blinking light for small amounts of time.

## Slide 7: BUMP TEST / CALIBRATION
G7 will let you know it’s time to bump or calibrate upon start up.
What do I do?
Press and hold
the up and down arrows to silence this reminder.
Then, bump or calibrate using one of the methods on the next slide.
Bump Test
Calibration

## Slide 8: BUMP TEST / CALIBRATION
With G7 Dock:
Place G7 in dock
Close the lid
Select bump test/calibration from the menu
Let G7 Dock do its thing!
You can bump and calibrate in one of two ways:
Manually:
Press OK to access the menu
Use the up and down arrows to navigate to bump test
Select bump test
Follow the steps on screen

## Slide 9: WEARING
Belt
Chest
DO NOT LEAVE G7 UNATTENDED WHEN POWERED ON, THIS CAN LEAD TO FALSE RED ALERTS

## Slide 10: YELLOW PENDING ALARM
What do I do?
Are you OK?
If yes, press the latch to return the device to normal function.
Fall detection
Check-in timer
No-motion
YELLOW PENDING ALARM

## Slide 11: YELLOW PENDING ALARM
What happens if you don’t tell the device you’re OK?
What do I do?
Press and hold the up and down arrows to mute the device.
Remember – this doesn’t cancel the alert.
YELLOW PENDING ALARM RED ALERT
If you don’t confirm you’re OK, the Yellow Pending Alarm escalates into Red Alert and notifies monitoring personnel.

## Slide 12: SOS ALERT
If you need to request help right away, you can trigger a SOS Alert.
What do I do?
Pull the latch!
How do I silence the alarm?
Press and hold the up and down arrows.
Remember – this does not cancel the alert.

## Slide 13: RED GAS ALERT
G7 is informing you of something dangerous in your environment.
For real-time customers, certain gas alerts will automatically generate a red alert and notify monitoring personnel.
What do I do?
Evacuate the area. When it is safe to do so, press and hold the up and down arrows to mute G7’s lights and sounds.
HIGH ALERT
OL (OVER LIMIT)
STEL (SHORT TERM
EXPOSURE
LIMIT)
TWA (TIME
WEIGHTED
AVERAGE)

## Slide 14: LIVE RESPONSE
What do I do?
Nothing! Wait for monitoring personnel to call or message you, and then let them know if you’re OK or if you need help.
LIVERESPONSE
The LiveResponse light will flash blue when monitoring personnel respond to your Alert using your company’s alert response protocol. When it shines on your device, it means someone will be contacting you to confirm you are OK.
Who are monitoring personnel?
Personnel are the Blackline Live Safety Agents or your own monitoring team.
?

## Slide 15: YELLOW WARNING ALARM
What do I do?
After you’ve read the screen, press and hold the up and down arrows to silence the device
New message
YELLOW WARNING ALARM
Low battery
Bump Test
Network Connection Interruption
Calibration
Low warning alarm for gas
Sensor error
Under limit
Pump block
Remember – Yellow warning alarms never escalate to Red Alerts. They are always between you and your device.

## Slide 16: MESSAGING
SENDING
Sending a message:
Press OK
Select send message
Scroll to the message you want to send, press OK.
Receiving a message:
Read your message
Press and hold the up and down arrows for 3 seconds
RECEIVING

## Slide 17: PUSH-TO-TALK – TRANSMITTING/RECEIVING
TRANSMITTING
Press and hold the red latch
When G7c finishes beeping, continue to hold and begin talking
When you’re finished talking, release the latch.
G7c will beep once more to let you know it’s done listening
RECEIVING
G7c will beep once to signal an incoming PTT message
G7c will play the message
G7c will beep once more when the message is done
NOTE: Be sure that you are talking into G7’s microphone, not the cartridge, to avoid false gas alarms.

## Slide 18: PUSH-TO-TALK - CHANNELS
Available Channels
Channels 0-99
Numbered channels for different groups of device users
Receive only
G7 only receives from all call and can’t transmit to any devices
All call
G7 Transmits to all PTT devices in
the organization and only receives from all call. This channel should only be used for safety supervisors.
CHANGING CHANNELS
1 2
3
Changing channels can be done from G7’s main or secondary menu.

## Slide 19: CONFIGURATION MODES
Available Modes
What is seen on your device is dependent on your configuration profile in Blackline Live
Normal mode
G7’s default for everyday operation
Pre entry
For checking an atmosphere before entering, with or without pump.
SCBA
For use with a supplied-air or self-contained breathing apparatus
Leak check
For checking an area for leaks, with or without pump.
High risk
For general high risk situations, like evacuations.
Pump run
Runs the pump continuously – such as for use in a hole-watch situation. A pump is required for this mode.
ENTERING A MODE
Entering a mode can be done from G7’s main or secondary menu.
When a mode is entered, G7’s screen will invert and the mode will be displayed in the top information banner.

## Slide 20: CONFIGURATION MODES
EXTENDING A MODE
When a mode timeout is reached, G7 will confirm that you’d like to stay in this mode.
What do I do?
Press the up arrow to extend the mode. Press the down arrow to exit the mode.
If you do not confirm that you would like to extend your mode within 30 seconds, G7 will return to normal mode, and if check-in is enabled, ask you to check in.
NOTE: High risk mode does not have a timeout, you must manually return to normal mode.

## Slide 21: G7 MULTI-PUMP CARTRIDGE
TURNING PUMP ON
Attach a multi-gas pump cartridge to G7
Enter a pumped mode, such as pre-entry or leak check
Perform a block test, following the steps on G7’s screen.
Pump will start automatically
NOTE: if the block test fails, the device will not enter the mode and pump won’t start.
TURNING PUMP OFF
Enter a non-pumped mode, such as normal, SCBA or high-risk.
Pump
Tubing
Quick-connect

## Slide 22: BLOCK TESTS
Block tests are performed to ensure your equipment is working properly before using pump to test the gas levels in an environment.
Blackline’s G7 multi-pump cartridge has two types of block tests:
AUTOMATIC BLOCK TEST
This is the block test that G7 runs through before entering a pumped mode.
The instructions for this block test appear on G7’s screen. If you pass the block test, G7 will enter the mode and pump will turn on.
If you fail the block test, G7 will return to normal mode.
MANUAL BLOCK TEST
This is the block test that you can perform anytime a pump is running.
To perform a manual block test:
Plug the end of your inlet
Wait for a yellow warning alarm
Unplug the end of your inlet
Wait for the alarm to stop
If the yellow warning alarm sounds when you plug, and stops when you release – your equipment is safe to use.
NOTE: G7 will go into yellow warning alarm when the pump is blocked during use.

## Slide 23: PUMP MENU OPTIONS
When a G7 multi-pump cartridge is attached, a new secondary menu and main menu option appear.
If the pump is on/off
Hose length (set from the pump options menu)
Flow rate (in real time, maintained by G7)
Sample timer (if enabled from pump options)
SECONDARY MENU
The pump secondary menu is available by pressing the down arrow button from G7’s main screen.
Here you will see things such as:
PUMP OPTIONS MENU
The pump options menu is available from G7’s main menu, under settings.
This is where you will set things such as:
Enabling/disabling sample timer
Hose length
Pump on Hose L: 10m 300 ml/min
Sample 70 sec.
Pump options
Back
Sample time ON Hose length

## Slide 24: CHARGING
G7c has an 18 hour battery life Remember to charge after every shift!
What do I do?
Put the clip into the base of the G7, then plug in the micro USB.

## Slide 25: QUESTIONS?

## Slide 26: support.BlacklineSafety.com
SUPPORT
CUSTOMER CARE
For technical support, please contact our Customer Care team.
North America (24 hours)
Toll Free: 1-877-869-7212
support@blacklinesafety.com
International (24 hours)
+1-403-452-0327
support@blacklinesafety.com